## Slide 1
EEG vs MEG
01
Implementation progress
EEG acquisition and experiment preparation
Theodoros Avgitidis
15 October 2026
Notes: This project investigates which motor and cognitive tasks a practical EEG setup can distinguish, with MEG task paradigms as a reference. The current implementation supports recording and inspection. A completed EEG–MEG performance comparison is not established by the project files.
Project sources:
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/planned-experiments.md
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/Einwilligungserklaerung_EEG-Studie.html
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/README.md

## Slide 2
Project aim and current scope
02
Which tasks can we distinguish with EEG?
Research aim
Compare actual movement, imagined movement and mental tasks.
Implemented
Record EEG, present instructions, label tasks and inspect signals.
Next research stage
Collect pilot data and evaluate task classification and MEG comparability.
Notes: The earlier study plan references MEGBCI2020 and includes word generation. The newer protocol dated 13 October focuses the pilot on movement, imagery, blinking and serial subtraction. Treat the latest protocol as the current pilot proposal. No classifier, MEG processing pipeline or microcontroller control implementation appears in the inspected project.
Project sources:
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/planned-experiments.md
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/experiment-protocol.md
/Users/theoa/Desktop/Projects/EEGvsMEG/analysis/view_eeg.py
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/main.cpp

## Slide 3
EEG connection and recording
03
Device setup
Find and connect the Unicorn headset. Inspect device details and select channels.
Recording modes
Capture short checks or continuous sessions, with an optional automatic stop.
Saved data
Export channel values and timing information to CSV at 250 samples per second.
Session monitoring
Check sample counts, recording errors and available device status indicators.
Notes: The terminal covers the supplied Unicorn API: version and error information, Bluetooth adapter information, paired/unpaired discovery, open/close, device information, channel configuration and index lookup, acquisition, data export, and optional digital output read/write. Digital outputs depend on device support. Production acquisition requires 64-bit Windows, the vendor DLL, Bluetooth and a compatible headset. Background recording reads blocks continuously and reports counter discontinuities plus battery and validation values if enabled. These values do not constitute a validated signal-quality score.
Project sources:
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/main.cpp
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/recorder.h
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/README.md

## Slide 4
Experiment organisation and task instructions
04
Experiment folders
Create, select and list experiments. Keep EEG files and task labels together.
Participant display
Show movement, subtraction or custom instructions in a separate Windows window.
Task markers
Log task labels during recording and update the participant display.
Data protection
Prevent accidental overwrites and experiment changes during acquisition.
Notes: The participant window supports a fixation cross, German hand/leg instructions, parameterised serial subtraction, arbitrary text and fullscreen mode. Marker labels can contain spaces and quotes. Markers use host timing and received sample counts. They indicate command processing and approximate sample positions, not exact stimulus onset or precise EEG–MEG synchronisation. Cues and timing are operator-driven. An automated trial scheduler is not implemented. Experiment names support Unicode and spaces, with checks against invalid names and paths.
Project sources:
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/cues.h
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/experiments.h
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/recorder.h
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/main.cpp

## Slide 5
Signal inspection and software checks
05
EEG viewer
Open recorded channels and task markers in MNE for visual inspection.
Display options
View signal traces or frequency spectra. Apply optional display filtering.
Input checks
Check units, sample numbering and invalid values. Warn about counter gaps.
Software testing
Simulated-device tests pass for recording, markers, file safeguards and failure handling.
Notes: The viewer accepts EEG 1–8 columns, asks explicitly for the recorded unit and converts values to volts for MNE. It imports event positions approximately from samples_received / 250. Optional filtering uses a 50 Hz notch and 0.5–30 Hz bandpass on a copy, preserving the CSV. It provides Welch frequency spectra. It does not implement artifact correction, feature extraction or classification. The hardware-free integration suite passed on 15 October 2026 in this workspace. It covers Unicode experiment names, path validation, switching guards, manual export, timed recording, CSV quoting, exclusive API access, overwrite prevention, continuous stop and simulated connection failure. This does not verify Bluetooth or real headset behaviour.
Project sources:
/Users/theoa/Desktop/Projects/EEGvsMEG/analysis/view_eeg.py
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/test_recorder.py
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/mock_api.cpp

## Slide 6
Study materials and proposed pilot
06
Prepared documentation
German operating guide
Headset and software summary
Participant information and consent
Task descriptions and pilot protocol
Latest pilot proposal
Actual arm and leg movement, blinking
Imagined arm and leg movement
Silent serial subtraction
Baseline recordings and recovery periods
112 task trials · About 29 minutes of measurement, or 38 minutes including planned breaks
Notes: The 13 October protocol is a proposed design, not an implemented automatic experiment. It specifies 60 physical-movement/blink trials, 40 imagery trials and 12 arithmetic trials, plus 60-second opening and closing baselines. Measurement totals 29:16 including within-trial recovery. Additional breaks total 9 minutes, giving 38:16 before setup, instruction and practice. The proposal specifies balanced task counts, randomisation constraints, saved seeds, trial lists and counterbalanced run orders. These remain protocol requirements rather than coded scheduler features. Word generation appears in earlier planning and is absent from the latest pilot. The participant information and consent document is prepared material, not evidence of institutional approval.
Project sources:
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/experiment-protocol.md
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/planned-experiments.md
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/plannedExperiments/README.md
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/manual/unicorn-hybrid-black-and-suite-summary.md
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/Einwilligungserklaerung_EEG-Studie.html
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/VERWENDUNG.md

## Slide 7
Remaining work and next steps
07
Pilot validation
Confirm headset behaviour, recording stability and instruction timing with participants.
Experiment automation
Implement the proposed trial sequence, randomisation and planned timing.
Scientific analysis
Define artifact handling and evaluate classifiers on held-out trials or blocks.
EEG–MEG comparison
Choose comparable tasks and evaluation measures, then assess performance.
Notes: The implemented tools provide a foundation for acquisition and visual inspection. They do not establish classification accuracy, validated neural effects or MEG equivalence. Physical movement and blinking can introduce muscle, movement and eye signals, so interpretation needs appropriate artifact handling. The protocol recommends keeping segments from the same trial together during evaluation and holding out entire participants for claims about new people. Precise synchronisation requires additional validation and potentially external timing hardware. Microcontroller control remains an application aim in the consent material, with no implementation found in the current project.
Project sources:
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/experiment-protocol.md
/Users/theoa/Desktop/Projects/EEGvsMEG/docs/Einwilligungserklaerung_EEG-Studie.html
/Users/theoa/Desktop/Projects/EEGvsMEG/gtec_Clib/terminal/README.md
/Users/theoa/Desktop/Projects/EEGvsMEG/analysis/view_eeg.py